## Slide 1: GNSS Signal Bands
1170
1180
1190
1200
1210
1220
1230
1240
1250
1260
1270
1280
1530
1540
1550
1560
1570
1580
1590
1600
1610
1620
1630
1575.42
L1P(Y)
L1C/A
L1C
1227.6
L2P(Y)
L2C
1176.45
1278.75
L5
E6
L6
L2C
1207.14
E1-B,C
L1C/A, L1S
L1C/B, L1C
1602 + 0.5625K
1246 +
0.4325K
L2OC
L5, L5S
1561.098
B1I
B1C
B2I
1268.52
B3I
L1-SPS
L5-SPS
L1C/A
L5
(MHz)
L3OC
L1C/A
1202.025
1600.995
1248.06
1050
1110
1150
1200
1250
1300
1350
1400
1450
1500
1550
1600
1650
GPS
GLONASS
Galileo
QZSS
NavIC
SBAS
BeiDou
L1
RF Bands
1191.795
E5a+b
E5a
E5b
B2a+b
B2a
B2b
L1OC
L2C/A
MSS (1525-1559)
RNSS (1164-1300)
L2/L5/
L6
RNSS
(1559-1610)
1290
LTE band 21 DL
(1495.9-1510.9)
1520
RNSS: Radionavigation Satellite Service
MSS: Mobile Satellite Service
Amateur Radio 23cm-band (1240-1300)
2490
2500
2480
2492.028
S-SPS
S

## Slide 2: GNSS Signals (1/3)
GPS [1][2][3] | 1575.42 | L1C/A | Q | -158.5 | BPSK(1) | 1023 | 1.023 | 1 | - | - | LNAV | 50 | 50 | - |  | L1CA
 |  | L1P(Y)*1 | I | -161.5 | BPSK(10) | 1week | 10.23 | 1week | - | - | LNAV | 50 | 50 | - |  | -
 |  | L1M | I | ? | BOC(10,5) | ? | 5.115 | ? | ? | ? | ? | ? | ? | ? | Block IIR-M~ | -
 |  | L1C-D | I | -163.0 | BOC(1,1) | 10230 | 1.023 | 10 | - | - | CNAV-2 | 100 | 50 | BCH,LDPC | GPS III~ | L1CD
 |  | L1C-P | I | -158.25 | TMBOC(6,1,4/33) | 10230 | 1.023 | 10 | 1800 | 18000 | - | - | - | - |  | L1CP
 | 1227.6 | L2C/A | Q | -164.5 | BPSK(1) | 1023 | 1.023 | 1 | - | - | LNAV | 50 | 50 | - | Block IIR-M~ | -
 |  | L2P(Y)*1 | I | -164.5/-161.5 | BPSK(10) | 1week | 10.23 | 1week | - | 1week | LNAV | 50 | 50 | - |  | -
 |  | L2M | I | ? | BOC(10,5) | ? | 5.115 | ? | ? | ? | ? | ? | ? | ? | Block IIR-M~ | -
 |  | L2C-M | Q/I | -160.0/ -158.5 | BPSK(1)+TDM | 10230 | 0.5115 | 20 | - | - | LNAV | 50 | 50 | - | Block IIR-M~ | -
 |  |  |  |  |  |  |  |  |  |  | CNAV | 50 | 25 | 1/2 *6 |  | L2CM
 |  | L2C-L |  |  | BPSK(1)+TDM | 767250 | 0.5115 | 1500 | - | - | - | - | - | - |  | (L2CL)
 | 1176.45 | L5-I | I | -157.9/-157.0 | BPSK(10) | 10230 | 10.23 | 1 | 10 (NH) | 10 | CNAV | 100 | 50 | 1/2 *6 | Block IIF~ | L5I
 |  | L5-Q | Q | -157.9/-157.0 | BPSK(10) | 10230 | 10.23 | 1 | 20 (NH) | 20 | - | - | - | - |  | L5Q
GLONASS [4][5][6][7] | 1602.0 + 0.5625K*2 | L1C/A*4 | I | -161.0 | BPSK(0.5) | 511 | 0.511 | 1 | - / 2*3 | - / 2*3 | GLO-STR | 100 | 50 | - |  | G1CA
 |  | L1P | Q | ? | BPSK(5) | 5110000 | 5.11 | 1000 | - | - | ? | ? | ? | - |  | -
 | 1600.995 | L1OCd | Q | ? | BPSK(1)+TDM | 1023 | 0.5115 | 2 | 2 (MC) | 4 | GLO-STR | 250 | 125 | 1/2 *6 | GLO-K2~ | G1OCD
 |  | L1OCp |  |  | BOC(1,1)+TDM | 4092 | 0.5115 | 8 | - | - | - | - | - | - |  | G1OCP
 |  | L1SC | I | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? |  | -
 | 1246.0 + 0.4375K*2 | L2C/A*5 | I | -167.0 | BPSK(0.5) | 511 | 0.511 | 1 | - / 2*3 | - / 2*3 | GLO-STR | 100 | 50 | - |  | G2CA
 |  | L2P | Q | ? | BPSK(5) | 5110000 | 5.11 | 1000 | - | - | ? | ? | ? | - |  | -
 | 1248.06 | L2CSI | Q | ? | BPSK(1)+TDM | ? | 0.5115 | ? | ? | ? | ? | ? | ? | ? | GLO-K2~ | -
 |  | L2OCp | Q | ? | BOC(1,1)+TDM | 10230 | 0.5115 | 20 | 50 | 1000 | - | - | - | - |  | G2OCP
 |  | L2SC | I | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? |  | -
 | 1202.025 | L3OCd | I | ? | BPSK(10) | 10230 | 10.23 | 1 | 5 (BC) | 5 | GLO-STR | 200 | 100 | 1/2 *6 | GLO-K1~ | G3OCD
 |  | L3OCp | Q | ? | BPSK(10) | 10230 | 10.23 | 1 | 10 (NH) | 10 | - | - | - | - |  | G3OCP
Galileo[8] | 1575.42 | E1-A | Q | ? | BOC(15,2.5) | ? | 2.5575 | ? | ? | ? | G/NAV | ? | ? | ? | PRS | -
 |  | E1-B | I | -157.0 | CBOC(6,1,1/11) | 4092 | 1.023 | 4 | - | - | I/NAV | 250 | 125 | 1/2 *6 | OS, SoL, CS | E1B
 |  | E1-C | I |  | CBOC(6,1,1/11) | 4092 | 1.023 | 4 | 25 | 100 | - | - | - | - |  | E1C
 | 1176.45 | E5a-I | I | -155.0 | BPSK(10) | 10230 | 10.23 | 1 | 20 | 20 | F/NAV | 50 | 25 | 1/2 *6 | OS, CS | E5AI
 |  | E5a-Q | Q |  | BPSK(10) | 10230 | 10.23 | 1 | 100 | 100 | - | - | - | - |  | E5AQ
 | 1207.14 | E5b-I | I | -155.0 | BPSK(10) | 10230 | 10.23 | 1 | 4 | 4 | I/NAV | 250 | 125 | 1/2 *6 | OS, SoL, CS | E5BI
 |  | E5b-Q | Q |  | BPSK(10) | 10230 | 10.23 | 1 | 100 | 100 | - | - | - | - |  | E5BQ
*1 AS ON, *2 K = {-7, ..., +6}, *3 Odd FCN, *4 L1OF, *5 L2OF, *6 Convolutional Code (R=1/2, K=7), NH: Neuman Hoffman Code, MC: Manchester Code, BC: Barker Code
System | Carrier Freq. (MHz) | Signal | I/Q | Min Rec. Power (dBW) | Modulation | Primary Code |  |  | Secondary Code |  | Navigation Data |  |  |  | Notes | Pocket SDR Signal ID
 |  |  |  |  |  | Length (chip) | Chip Rate (Mcps) | Cycle (ms) | Length (chip) | Cycle (ms) | Data | Symbol Rate (sps) | Data Rate (bps) | FEC |  | 
Military or Restricted Signal

## Slide 3: GNSS Signals (2/3)
Galileo (Cont.) | 1191.795 | E5a+b*7 | - | (-152.0) | 8-PSK(10) | 10230 | 10.23 | 1 | 100 | 100 | - | - | - | - |  | -
 | 1278.75 | E6-A | Q | ? | BOC(10,5) | ? | 5.115 | ? | ? | ? | G/NAV | ? | ? | ? | PRS | -
 |  | E6-B | I | -155.0 | BPSK(5) | 5115 | 5.115 | 1 | - | - | C/NAV | 1000 | 500 | 1/2 *6 | CAS, HAS | E6B
 |  | E6-C | I |  | BPSK(5) | 5115 | 5.115 | 1 | 100 | 100 | - | - | - | - |  | E6C
QZSS [9][10][11][12] | 1575.42 | L1C/A | I/Q | -158.5*8 | BPSK(1) | 1023 | 1.023 | 1 | - | - | LNAV | 50 | 50 | - |  | L1CA
 |  | L1C/B | I | -158.5 | BOC(1,1) | 1023 | 1.023 | 1 | - | - | LNAV | 50 | 50 | - |  | L1CB
 |  | L1C-D | I | -163.0*9 | BOC(1,1) | 10230 | 1.023 | 10 | - | - | CNAV2 | 100 | 50 | BCH,LDPC |  | L1CD
 |  | L1C-P | Q | -158.25 | BOC(1,1) | 10230 | 1.023 | 10 | 1800 | 18000 | - | - | - | - | Block I | L1CP
 |  |  | I | -158.25*10 | TMBOC(6,1,4/33) | 10230 | 1.023 | 10 | 1800 | 18000 | - | - | - | - | Block II ~ | L1CP
 |  | L1S | I | -161.0/-158.5 | BPSK(1) | 1023 | 1.023 | 1 | - | - | L1S | 500 | 250 | 1/2 *6 | SLAS | L1S
 | 1227.6 | L2C-M | I | -160.0/ -158.5 | BPSK(1)+TDM | 10230 | 0.5115 | 20 | - | - | CNAV | 50 | 25 | 1/2 *6 |  | L2CM
 |  | L2C-L |  |  | BPSK(1)+TDM | 767250 | 0.5115 | 1500 | - | - | - | - | - | - |  | (L2CL)
 | 1176.45 | L5-I | I | -157.9/-157.0 | BPSK(10) | 10230 | 10.23 | 1 | 10 (NH) | 10 | CNAV | 100 | 50 | 1/2 *6 |  | L5I
 |  | L5-Q | Q | -157.9/-157.0 | BPSK(10) | 10230 | 10.23 | 1 | 20 (NH) | 20 | - | - | - | - |  | L5Q
 |  | L5S-I | I | -157.0*11 | BPSK(10) | 10230 | 10.23 | 1 | - | - | L5S | 500 | 250 | 1/2 *6 | Normal mode | L5SI
 |  |  |  |  |  |  |  |  | 2 (MC) | 2 | L5S | 500 | 250 | 1/2 *6 | Verif. mode | L5SIV
 |  | L5S-Q | Q |  | BPSK(10) | 10230 | 10.23 | 1 | 20 (NH) | 20 | - | - | - | - | Normal mode | L5SQ
 |  |  |  |  |  |  |  |  | 2 (MC) | 2 | - | - | - | - | Verif. mode | L5SQV
 | 1278.75 | L6D | I | -155.7 | BPSK(5)+TDM*12 | 10230 | 2.5575 | 4 | - | - | L6D | 2000 | 2000 | RS | CLAS | L6D
 |  | L6L |  |  | BPSK(5)+TDM | 1048575 | 2.5575 | 410 | 2 (MC) | 820 | - | - | - | - | Block I | -
 |  | L6E |  |  | BPSK(5)+TDM*12 | 10230 | 2.5575 | 4 | - | - | L6E | 2000 | 2000 | RS | MADOCA-PPP | L6E
BeiDou [13][14][15] [16][17] | 1561.098 | B1I | I | -163.0 | BPSK(2) | 2046 | 2.046 | 1 | 20 (NH) | 20 | D1 | 50 | 50 | BCH |  | B1I
 |  |  |  |  |  |  |  | 1 | - | - | D2 | 500 | 500 | BCH | GEO | B1I
 |  | B1Q | Q | ? | BPSK(2) | ? | 2.046 | ? | ? | ? | ? | ? | ? | ? |  | -
 | 1575.42 | B1C-D | I | -159.0/ -161.0 | BOC(1,1) | 10230 | 1.023 | 10 | - | - | B-CNAV1 | 100 | 50 | NB-LDPC | BDS-3 | B1CD
 |  | B1C-P | I |  | QMBOC(6,1,4/33) | 10230 | 1.023 | 10 | 1800 | 18000 | - | - | - | - |  | B1CP
 |  | B1A-D | Q | ? | BOC(14,2) | ? | 2.046 | ? | ? | ? | ? | ? | ? | ? |  | -
 |  | B1A-P | Q |  |  | ? | 2.046 | ? | ? | ? | - | - | - | - |  | -
 | 1176.45 | B2a-D | I | -156.0/ -158.0 | BPSK(10) | 10230 | 10.23 | 1 | 5 | 5 | B-CNAV2 | 50 | 25 | NB-LDPC | BDS-3 | B2AD
 |  | B2a-P | Q |  | BPSK(10) | 10230 | 10.23 | 1 | 100 | 100 | - | - | - | - |  | B2AP
 | 1207.14 | B2I | I | ? | BPSK(2) | 2046 | 2.046 | 1 | 20 (NH) | 20 | D1 | 50 | 50 | BCH |  | B2I
 |  |  |  |  |  |  |  | 1 | - | - | D2 | 500 | 500 | BCH | GEO | B2I
*7 AltBOC, *8 -164.0 dBW (SVID=7), *9 -167.2 dBW (SVID=7), *10 -162.4 dBW (SVID=7), *11 -162.6 dBW (SVID=3), *12 +CSK by Nav Data
System | Carrier Freq. (MHz) | Signal | I/Q | Min Rec. Power (dBW) | Modulation | Primary Code |  |  | Secondary Code |  | Navigation Data |  |  |  | Notes | Pocket SDR Signal ID
 |  |  |  |  |  | Length (chip) | Chip Rate (Mcps) | Cycle (ms) | Length (chip) | Cycle (ms) | Data | Symbol Rate (sps) | Data Rate (bps) | FEC |  | 
Military or Restricted Signal

## Slide 4: GNSS Signals (3/3)
BeiDou (Cont.) | 1207.14 | B2Q | Q | ? | BPSK(10) | 10230 | 10.23 | 1 | ? | ? | ? | ? | ? | ? |  | -
 | 1207.14 | B2b-I | I | -160.0/ -162.0 | BPSK(10) | 10230 | 10.23 | 1 | - | - | B-CNAV3 | 1000 | 500 | NB-LDPC | BDS-3 | B2BI
 |  |  |  |  |  |  |  |  |  |  | B2b-PPP | 1000 | 500 | NB-LDPC | BDS-3, GEO | B2BI
 |  | B2b-Q | Q | ? | BPSK(10) | 10230 | 10.23 | 1 | ? | ? | ? | ? | ? | ? | BDS-3 | -
 | 1191.795 | B2a+b*13 | - | ? | 8-PSK(10) | 10230 | 10.23 | 1 | ? | ? | - | - | - | - |  | -
 | 1268.52 | B3I | I | -163.0 | BPSK(10) | 10230 | 10.23 | 1 | 20 (NH) | 20 | D1 | 50 | 50 | BCH |  | B3I
 |  |  |  |  |  |  |  | 1 | - | - | D2 | 500 | 500 | BCH | GEO | B3I
 |  | B3Q | Q | ? | BPSK(10) | ? | 10.23 | ? | ? | ? | ? | ? | ? | ? |  | -
 |  | B3A-D | I | ? | BPSK(10) | ? | 10.23 | ? | ? | ? | ? | ? | ? | ? | BDS-3 | -
 |  | B3A-P | I |  | BPSK(10) | ? | 10.23 | ? | ? | ? | - | - | - | - |  | -
NavIC [18][19] | 1575.42 | L1-SPS-D | Q | -159.6 | BOC(1,1) | 10230 | 1.023 | 10 | - | - | IRN-NAV | 100 | 50 | BCH,LDPC | NVS-01~ | I1SD
 |  | L1-SPS-P | I | -158.2 | CSBOC(6,1,4/33) | 10230 | 1.023 | 10 | 1800 | 18000 | - | - | - | - |  | I1SP
NavIC [18][19] | 1176.45 | L5-SPS | *14 | -159.0 | BPSK(1) | 1023 | 1.023 | 1 | - | - | IRN-NAV | 50 | 25 | 1/2 *6 |  | I5S
 |  | L5-RS-D | *14 | ? | BOC(5,2) | ? | 2.046 | ? | ? | ? | ? | 50 | 25 | 1/2 *6 |  | -
 |  | L5-RS-P | *14 | ? | BOC(5,2) | ? | 2.046 | ? | ? | ? | - | - | - | - |  | -
 | 2492.028 | S-SPS | *14 | -162.3 | BPSK(1) | 1023 | 1.023 | 1 | - | - | IRN-NAV | 50 | 25 | 1/2 *6 |  | (ISS)
 |  | S-RS-D | *14 | ? | BOC(5,2) | ? | 2.046 | ? | ? | ? | ? | 50 | 25 | 1/2 *6 |  | -
 |  | S-RS-P | *14 | ? | BOC(5,2) | ? | 2.046 | ? | ? | ? | - | - | - | - |  | -
SBAS *15 [20] | 1575.42 | L1C/A | I | - | BPSK(1) | 1023 | 1.023 | 1 | - | - | SBAS | 500 | 250 | 1/2 *6 | PRN120-158 | L1CA
 | 1176.45 | L5-I | I | - | BPSK(10) | 10230 | 10.23 | 1 | 2 (MC) | 2 | L5 SBAS | 500 | 250 | 1/2 *6 |  | L5I
 |  | L5-Q | Q | - | BPSK(10) | 10230 | 10.23 | 1 | 2 (MC) | 2 | - | - | - | - |  | L5Q
[1] IS-GPS-200K, Navstar GPS space segment/navigation user interfaces - interface specification, 2019, [2] IS-GPS-800F, Navstar GPS space segment/user segment L1C interface - interface specification, 2019, [3] IS-GPS-705A, Navstar GPS space segment/user segment L5 interface - interface specification, 2010, [4] GLONASS interface control document - navigation radiosignal in bands L1, L2, version 5.1, 2008, [5] GLONASS interface control document - code division multiple access open service navigation signal in L1 frequency band, edition 1.0, 2016, [6] GLONASS interface control document - code division multiple access open service navigation signal in L2 frequency band, edition 1.0, 2016, [7] GLONASS interface control document - code division multiple access open service navigation signal in L3 frequency band, edition 1.0, 2016, [8] European GNSS (Galileo) open service signal-in-space interface control document (OS SIS ICD), Issue 1, Revision 3, 2016, [9] Quasi-Zenith satellite system interface specification - satellite positioning, navigation and timing service (IS-QZSS-PNT-003), 2018, [10] Quasi-zenith satellite system interface specification - sub-meter level augmentation service (IS-QZSS-L1S-003), 2018, [11] Quasi-zenith satellite system interface specification - centimeter level augmentation service (IS-QZSS-L6-003), 2018, [12] Quasi-zenith satellite system interface specification - positioning technology verification service (IS-QZSS-TV-004), 2023, [13] BeiDou navigation satellite system signal in space interface control document - open service signal B1I, version 3, 2019, [14] BeiDou navigation satellite system signal in space interface control document - open service signal B1C, version 1.0, 2017, [15] BeiDou navigation satellite system signal in space interface control document - open service signal B2a, version 1.0, 2017, [16] BeiDou navigation satellite system signal in space interface control document - open service signal B3I, version 1.0, 2018, [17] BeiDou navigation satellite system signal in space interface control document - Precise Point Positioning service signal PPP-B2b, version 1.0, 2020, [18] Indian Regional Navigation Satellite System, Signal in space ICD for standard positioning service version 1.1, 2017, [19] NAVIC signal in space ICD for standard positioning service in L1 frequency version 1.0, 2023, [20] RTCA, Minimum Operational Performance Standards for Airborne Equipment Using Global. Positioning System/Wide Area Augmentation System, DO-229, 1996
*13 ACE-BOC, *14 Interplex Modulation, *15 including QZSS L1Sb, BeiDou BDSBAS-B1C/B2a
System | Carrier Freq. (MHz) | Signal | I/Q | Min Rec. Power (dBW) | Modulation | Primary Code |  |  | Secondary Code |  | Navigation Data |  |  |  | Notes | Pocket SDR Signal ID
 |  |  |  |  |  | Length (chip) | Chip Rate (Mcps) | Cycle (ms) | Length (chip) | Cycle (ms) | Data | Symbol Rate (sps) | Data Rate (bps) | FEC |  | 
Military or Restricted Signal